## Slide 1: MIPS 16 Bit Processor
By:
Robert Maxwell
&
Ryan Agudelo

## Slide 2: MIPS Machine
Microprocessor without Interlocked Pipeline Stages (MIPS)
Reduced instruction set computer (RISC)
  Simplified instructions can provide higher performance if the simplicity enables faster execution of each instruction
Instruction set architecture (ISA)
  Architecture related to programming
    Native data types
    Instructions
    Registers
    Addressing modes

## Slide 3: Pipelined MIPS, showing the five stages (instruction fetch, instruction decode, execute, memory access and write back)
MIPS Diagram

## Slide 4: Instruction Set
Assumptions:
Subset of MIPS 1 ISA
Byte/Word = 8/16 bits
All instructions have
  R (register), I (immediate) or
  J (jump) format.
No Floating Point Co-Processor
Minimum instruction (256 bytes and data memory(512 bytes)

## Slide 5: Verilog-HDL Design Procedure
Code the initial hardware and control signals
Test each arithmetic state to verify appropriate functionality
Test Branch functionality
Alter design (if needed – then re-test)
Test for correctness of data
Alter design (if needed – then re-test)
Test the circuit with a program that proves correct operation

## Slide 6: Initial Design
Courtesy of Dr. Byeong Lee : Microcomputer Architecture Lectures (UTSA)

## Slide 7: Test Code (Arithmetic)
Instruction | Instruction Code | Expected Result
ADD $1,$2,$3 | 0x00430820 | R1 = 0x00000005
SUB $4,$5,$3 | 0x00A32022 | R4 = 0x00000002
ADDI $6,$2,100 | 0x20460064 | R6 = 0x00000066
ADDU $7,$5,$5 | 0x00A53821 | R7 = 0x0000000A
SUBU $8,$3,$3 | 0x00634023 | R8 = 0x00000000
ADDIU $9,$2,100 | 0x24490064 | R9 = 0x00000066
AND $10,$21,$22 | 0x02B65024 | R10=0x00000014
OR $11,$21,$22 | 0x02B65825 | R11=0x00000017
ANDI $12,$21,100 | 0x32AC0064 | R12=0x00000004
ORI $13,$21,100 | 0x36AD0064 | R13=0x00000075
SLL $14,$2,10 | 0x00407280 | R14=0x00000800
SRL $15,$31,5 | 0x03E07942 | R15=0x00000001
LW $16,$7,9 | 0x8CF00009 | R16=0x00000013
SW $6,$8,10 | 0xAD06000A | MEM[100] = 0x66
LUI $17,100 | 0x3C110064 | R17=0x00640000

## Slide 8: ADD to AND (Immed16)

## Slide 9: OR (Immed16) to Load Upper (Immed16)

## Slide 10: Initial Results
Register File
Memory
Expected Result
R1 = 0x00000005
R4 = 0x00000002
R6 = 0x00000066
R7 = 0x0000000A
R8 = 0x00000000
R9 = 0x00000066
R10=0x00000014
R11=0x00000017
R12=0x00000004
R13=0x00000075
R14=0x00000800
R15=0x00000001
R16=0x00000013
MEM[100] = 0x66
R17=0x00640000

## Slide 11: Branch Hazards
If the Branch is taken, next 3 instructions must be burned and flushed from the Pipeline
Courtesy of Dr. Byeong Kil Lee : Microcomputer Architecture Lectures (UTSA)

## Slide 12: Branch Hazard Example
Branch destination gets loaded 4 cycles after decision

## Slide 13: Solutions
Branch Prediction – Many options possible (predict taken, not taken, 2-bit predictor, other algorithms[2])
  For this design, we predict not taken
Move branch decision hardware to the ID stage so as to only incur a 1 cycle penalty

## Slide 14: Branch Decision to ID Stage
Adapted from Dr. Byeong Kil Lee : Microcomputer Architecture Lectures (UTSA)

## Slide 15: Data Hazards
Occurs when the result of an instruction is required for a subsequent instruction
Courtesy of Dr. Byeong Kil Lee : Microcomputer Architecture Lectures (UTSA)

## Slide 16: Solution
Add hardware to the EX stage that tests the destination and source register addresses to determine if the result of an operation is needed by the next few instructions.
Here we compare source1 (EX stage) with source2 (EX stage) with reg_dest (MEM stage) and reg_dest (WB stage)

## Slide 17: Completed Design
Adapted from Dr. Byeong Kil Lee : Microcomputer Architecture Lectures (UTSA)

## Slide 18: Final Design Test Code
Takes sum first ‘n’ Fibonacci numbers and saves to memory[3]
HEX Code
Fib: addi $3,$0,8 // init $3 = n 0x20030008
addi $4,$0,1 //$4 = 1 0x20040001
addi $5,$0,-1 //$5 = -1 0x2005FFFF
Loop: beq $3,$0,end //if $3==0, branch 0x10600008
add $4,$4,$5 //$4 = $4 + $5 0x00852020
sub $5,$4,$5 //$5 = $4 - $5 0x00852822
addi $3,$3,-1 //$3 = $3 – 1 0x2063FFFF
j Loop // jump 0x0800000C
nop 0x00000000
End: stw $4,32($0) //store final value 0xAC040020

## Slide 19: Expected Values
n | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
$3 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
$4 | 0 | 1 | 1 | 2 | 3 | 5 | 8 | 13 | Break
$5 | -1 | 1 | 0 | 1 | 1 | 2 | 3 | 5 | 8
MEM | Prev. | Prev. | Prev. | Prev. | Prev. | Prev. | Prev. | Prev. | 13

## Slide 20: Simulation Results

## Slide 22
TTL Cycles: 56 Instr. Count: 47 Branch Stalls: 9
IPC: 0.84

## Slide 23: Memory Results
Register File
Data Memory

## Slide 24: Encounter Layout
Pre Nanoroute
Post Nanoroute

## Slide 25: Cadence Encounter
Area
  Chip Area: 2.82 x 2.82cm
  Core Area: 2.75 x 2.75cm
  Standard Cell Area: 1.94 x 1.94cm
Power
  Internal: 26.26mW
  Leakage: 8.604mW
  Total: 34.88mW
  Switching: 0.01144mW
Timing
  WNS : -26.113ns
  TNS: -1708.0ns

## Slide 26: Cell Layout
Amoeba Space Allocation Layout
Instance Cells Cell Area Net Area Wireload
---------------------------------------------------------------------------
mips_16b 15551 375753 0 <none> (D)
MEM 7618 203965 0 <none> (D)
54%
IF 3037 50432 0 <none> (D)
13%
ID 2951 67815 0 <none> (D)
18%
EX 1103 19064 0 <none> (D)
5%

## Slide 27: Schematics
RTL Generated Schematic
Complete Encounter Generated Schematic

## Slide 28: Power
Layer Name | Area of Power Net | Routable Area | Percentage
Metal1 | 60802.0000 | 756898.0524 | 8.0331%
Metal2 | 1536.8672 | 756898.0524 | 0.2030%
Metal3 | 782.8832 | 756898.0524 | 0.1034%
Metal4 | 0.0000 | 756898.0524 | 0.0000%
Metal5 | 0.0000 | 756898.0524 | 0.0000%
Metal6 | 0.0000 | 756898.0524 | 0.0000%
Area of Power Net Distribution
Compiler GUI Yielded some interesting details
bash% rc –f <gfile>.g -gui

## Slide 29: Physical Chip Characteristics
Wire Length Distribution | 
Total Metal1 wire length | 46548.3450 um
Total Metal2 wire length | 311237.6350 um
Total Metal3 wire length | 372118.1150 um
Total Metal4 wire length | 194577.3200 um
Total Metal5 wire length | 71558.7500 um
Total Metal6 wire length | 15791.4500 um
Total wire length | 1011831.6150 um ≈ 40 inches
Average wire length/net | 56.1629 um

## Slide 30: Summary
Prototype MIPS_16B:
  Library: tsmc18 – 0.18um tech
  Vdd: 1.8Vdc
  Total Area: 2.82 x 2.82cm
  Total Power: 34.88mW
  Pin Count: 540 ext. pins

## Slide 31: Questions?

## Slide 32: Bibliography
[1] Dr. Byeong Lee, Computer Architecture Lectures, Lecture 3 – Pre_0,1,2,3 MIPS, University of Texas at San Antonio, Feb. 09, 2011.
[2] Hennessy, John and Patterson, David. Computer Architecture: A Quantitative Approach, 4th Edition. San Francisco: Elsevier,2007
[3] David Harris, Introduction to VLSI, Lecture 2: MIPS processor example, Harvey Mudd College, http://www.cmosvlsi.com/lect2.pdf, Spring 2004